## Slide 1: Time Sync Overview

## Slide 2: Agenda
What is Time Sync?
Time Sync supported features
Time Sync not supported features
Time Sync stack diagram
  PTP stack to application layer
  Time Sync HAL to PTP stack layer
  APIs from Low level driver layer
Time Sync PTP Sequence diagram
Multi-core Time-synchronization design

## Slide 3: What is Time Sync?
Time Sync is a PDK transport library developed to provide uniform IP abstracted PTP support to CPSW & ICSS IPs.
Time Sync library utilizes hardware timestamping provided by CPTS(CPSW) or IEP(ICSS) to enable time synchronization with better accuracy
Time Sync library consists of two parts:
  Time Sync HAL
  Time Sync Protocol (PTP)
Time Sync HAL:
HAL provides an uniform API to the protocol layer by abstracting CPSW and EMAC APIs
HAL provides Timer and PTP frame transmission/reception APIs
Time Sync Protocol:
Protocol layer implements TI-RTOS based PTP stack with generic time sync capabilities

## Slide 4: Time Sync supported features
Configurations expected from application:
  Device configurations: Master/Boundary/Transparent/Ordinary slave
  Step-mode configuration: Two-step
  Network protocol: IEEE802.3.
  Delay mechanism: P2P
  PPS configuration
APIs expected from Low-level network driver:
  DMA APIs:
    Tx & Rx packet submit/retrieve functions
    Tx & Rx event notify
  Hardware timer functions:
    Get Tx/Rx timestamp
    Get time, Set time
    Periodic pulse
    Set compensation (PPM)

## Slide 5: Time Sync not supported features
Best Master Clock algorithm
  Currently, the first announce message sender is assumed as master
PTP management frame handling
IPv4/ IPv6 PTP frame handling
Not tested on CPSW2G, AM3xxx/AM4xxx/AM5xxx platforms

## Slide 6: Time Sync stack diagram
PTP stack to application APIs
Comparison with Linux PTP
Linux PTP | TimeSync PTP
ptp4l | TimeSync_initPtp
phc2sys | TimeSync_coupleTimer
pmc | TimeSync_ptpMgmt
pps | TimeSync_configPps
1
2
3
1
TimeSync driver layer refers to Time sync HAL abstracting underlying network driver layer

## Slide 7
Timer APIs
SoC/ Use case specific APIs
Packet Tx/Rx APIs APIs
TimeSync_getTxTimestamp(hTimeSync, txFrameType, txPort, seqId, &nanoseconds, &seconds)
TimeSync_getRxTimestamp(hTimeSync, rxFrameType, rxPort,seqId, &nanoseconds, &seconds)
TimeSync_getCurrentTime(hTimeSync, &nanoseconds, &seconds)
TimeSync_setClockTime(hTimeSync, nanoseconds, seconds)
TimeSync_adjTimeSlowComp(hTimeSync, adjOffset, interval)
TimeSync_getPtpFrame(hTimeSync, &buff, &size, &portNum)
TimeSync_sendPtpFrame(hTimeSync, &buff, size, portNum)
hTimeSync = TimeSync_open(&timeSyncConfig)
For AM335x & AM437x
TimeSync_ecapEdmaConfig(ecapEdmaConfig)
APIs to PTP stack layer
Timer APIs
Pkt Tx/Rx APIs
SoC specific APIs
PTP Stack
Time Sync driver layer
PTP stack layer
2

## Slide 8
Timer APIs
DMA APIs
SOC/IP specific APIs
CPSW LLD
IEP LLD
CPTS
IEP
Hardware layer
Network driver layer
Time Sync driver layer
TimeSync API | CPSW API | ICSS API
TimeSync_getTxTimestamp | CPSW_CPTS_IOCTL_LOOKUP_EVENT | IEP register read/writes
TimeSync_getRxTimestamp | CPSW_CPTS_IOCTL_LOOKUP_EVENT | “”
TimeSync_getCurrentTime | CPSW_CPTS_IOCTL_PUSH_TIMESTAMP_EVENT | “”
TimeSync_setClockTime | CPSW_CPTS_IOCTL_LOAD_TIMESTAMP | “”
TimeSync_adjTimeSlowComp | CPSW_CPTS_IOCTL_SET_TS_PPM | “” (For AM335x & AM437x ECAP config API)
TimeSync_getPtpFrame | CpswDma_retrieveRxPackets | ICSS_EmacRxPktGet
TimeSync_sendPtpFrame | CpswDma_submitTxReadyPackets | ICSS_EmacTxPacket
APIs from Low level driver layer
3

## Slide 9: Time Sync Configuration (parameters from PTP to HAL)
timeSyncConfig
protocolConfig
frameNotifyCfg
socConfig
protocol
(Annex D/E/F )
deviceCfg
(MC/OC/TC/BC)
StepMode
VLAN Configuration
PPS configuration
(PPS: interval, callback function)
Port mask
txNotifyCb
txNotifyCbArg
rxNotifyCb
rxNotifyCbArg
socVersion
ipVersion

## Slide 10: Sequence diagram
Application
TimeSync PTP
TimeSync HAL
Network driver
TimeSyncPtp_init(ptpCfg)
TimeSync_open(&timeSyncConfig)
Configure timer
Configure DMA (register callbacks)
SoC specific configurations
Return hTimeSync
Store hTimeSync
PTP frame
Call registered rxNotfiyCallbackFxn
TimeSync_getPTPframe(hTimeSync, &buff, &size, &portNum)
CpswDma_retrieveRxPackets / ICSS_EmacRxPktGet
Retrieve and return packet
TimeSync_getRxTimestamp(hTimeSync, rxFrameType, rxPort,seqId, &nanoseconds, &seconds)
PTP stack process received frame and sends response if required
TimeSync_sendPtpFrame(hTimeSync, &buff, size, portNum)
CpswDma_submitTxReadyPackets / ICSS_EmacTxPktGet
Call registered txNotfiyCallbackFxn
TimeSync_getTxTimestamp(hTimeSync, txFrameType, txPort, seqId, &nanoseconds, &seconds)
PTP stack computes
clock correction offset
TimeSync_setClockTime(hTimeSync, nanoseconds, seconds)
PTP stack performs ToD synchronization,
Calculates drift correction
PPS interrupt
Call registered PPS callback function
TimeSync_adjTimeSlowComp(hTimeSync, adjOffset)

## Slide 11: Multi – core Time Synchronization (similar to phc2sys in Linux)
Time Sync Router Configuration
Time-sensitive
Application
CPTS Timer
Remote core’s Timer
Coupling is done periodically
TSR
CPTS
Remote
core
Hw Push
64-bit Time Stamp
GTC0/ TIMER[14-19]
GTC0
TIMER[14-19]
PWM
Remote Core
Coupling between remote core’s timer and CPTS timer is done through Hardware push events of CPTS and Time Sync Router(TSR).
With this a linear relation is established between CPTS & remote timer.
Once the relation is established, remote core can independently use this coupled timer.

## Slide 12: Multi – core Time Synchronization (similar to phc2sys in Linux)
iproute2
brctl
ethtool
vconfig
tc
mstpd
lldpd
snmpd
lacp
mvrp
Bonds
Bridges
VXLAN
RT Netlink
ethtool ioctl
switchdev driver
swp0
swp1
swp7
cpsw driver
swp1
Remote Configuration Client
Remote Configuration Client
CPSW_9G
CPSW 9G Register
EAPOL
Remote Configuration Server
Firmware Application API
TI-RTOS
IP Router
NDK
CPSW_LLD
Other Drivers
Main R5 (switch)
ALE
LLD
ENETPHY
LLD
Apps
CPTS
LLD
Grand Master
Time Sync
Time Sync SW
Call to Register the Remote Timer with the CPTS timer
Direct Control Path
IPC Control Path
Direct Data Path
Ethernet Firmware (AUTO)
Demo app
Kernel driverr
PDK CPSW LLD (AUTO)
Switch resident protocols
Time Sync provides get Time and Lookup event APIs to remote cores via existing rpmsg layer.
Using UDMA descriptor metadata, any Tx/Rx packet can also be time-stamped by CPTS.
In addition to this, remote core can use its local synchronized timer for getting current time.
Remote core

## Slide 13: Multi – core Time Synchronization sequence
Remote core
EthFw(with TimeSync)
Sets up DM TIMER[14-19] / GTC0 and enable periodic PWM output/ HW push output
Register HW Push
4. Allocates a Hardware Push Instance.
  Configures TSR to map the DM Timer’s PWM to the HW Push Instance
  Save the callback for the Hardware Push Instance
R5 runs PTP and synchronizes with the external master clock
When hardware push event occurs, remote core’s registered callback is called with CPTS timer value.
Call back with Event Info
Hw Push Time stamp value N
Hw Push Time stamp value N+1
With two consecutive Hw push Time stamp values, the DMTIMER/GTC to CPTS clock rate ratio and linear relationship are established.
IPC
Call CpswProxy_registerRemoteTimer with timer Information & call back function.
Call back with Event Info
Next Hw Push event
– Synchronized Time (CPTS time)
– Rate ratio
– Local Timer Value
– Constant value
.
.
.

## Slide 14
© Copyright 2020 Texas Instruments Incorporated. All rights reserved.
This material is provided strictly “as-is,” for informational purposes only, and without any warranty.
Use of this material is subject to TI’s Terms of Use, viewable at TI.com